## Slide 1: MODFLOW 6—LGR
Introduction to Groundwater Modeling using MODFLOW
January 9-13, 2022
SDSU, San Diego, California

## Slide 2: Local Grid Refinement
Why use LGR?
  Resolution can be increased in areas of interest
  Can be used with regular MODFLOW grids
  Child models can be extracted and run separately
Why not use it?
  More complicated to work with
  Concerns about accuracy
  Limited GUI support
  It used to be relatively slow and could have convergence problems

## Slide 3: Approaches
Old School (Telescopic Mesh Refinement)
  Heads or flows from a parent model are used to set boundary conditions for a child model
MODFLOW-LGR
  Parent and child models are iteratively coupled
MODFLOW-USG
  Parent and child models are built into a single mesh
MODFLOW 6
  Parent and child models are solved simultaneously in a single matrix solution

## Slide 4: 1. TMR
Heads or flows from parent model used as boundary conditions for child model
Easy to do
Some GUI support (e.g. Groundwater Vistas)
Also supported in modflow-setup python code
Child does not have to be coincident with parent
No automatic feedback from child to parent

## Slide 5: 2. MODFLOW-LGR
Parent and child models are iteratively coupled
Child models can be used separately
May be slow convergence
Limited GUI support
Restrictions on parent/child configurations

## Slide 6: 3. MODFLOW-USG
Parent, child, grandchildren, cousins, etc. are built into a single mesh
Some GUI support
Everything solved in a single matrix (fast and robust)
Need to reconstruct mesh to add a new child

## Slide 7: 4. MODFLOW 6
Can do single mesh or multiple models
Everything solved in a single matrix (fast and robust)
No present GUI support

## Slide 8: MODFLOW 6 LGR
Construct parent and child models
Use IDOMAIN to inactivate parent model where child model exists
Use the GWF6-GWF6 Exchange (specified in mf6.nam) to couple the models

## Slide 9: GWF6-GWF6 Exchange

## Slide 10: Map View
cl1
cl2
hwva
Cell in model 1
Cell in model 2
ihc = 1 or 2 (horizontal connection)

## Slide 11: Cross-Section View
TOP
BOT
ihc = 1
TOP
BOT
ihc = 2
“vertically staggered”

## Slide 12: Vertical Connections
hwva is the area of the connection
ihc = 0
cl1 is the half cell thickness of the cell in model 1
cl2 is the half cell thickness of the cell in model 2

## Slide 13: McDonald Valley Problem