## Slide 1: MODFLOW 6—Transport and Variable-Density Flow
Introduction to Groundwater Modeling using MODFLOW
January 9-13, 2023
SDSU, San Diego California

## Slide 2: MODFLOW 6 GWF + MT3D-USGS
MT3D-USGS developed and maintained in cooperation with S.S. Papadopulos & Associates Inc.
Works with standard head and budget files produced by MODFLOW 6
Regular MODFLOW grids
Notes: Many of you are probably familiar with MT3D-USGS, which is a collaborative effort between SSPA and the USGS
I’ve been using MT3D for about 30 years, and I think it’s a great program. In my earlier life I worked with Weixing Guo to couple MT3D and MODFLOW to create SEAWAT.
The purpose of this slide is to let you know that MT3D-USGS works with the output from MODFLOW 6 (for a regular grid and a couple other restrictions).
We’ve had a fair number of compatibility problems over the years with the Flow-Transport-Link File (though they should mostly be fixed now)
Our approach here was to have MT3D-USGS work directly with the output files from MODFLOW 6 rather than writing a separate FTL file.

## Slide 3: Groundwater transport (GWT) Model

## Slide 4: MODFLOW 6 Groundwater Transport Model
First released October 2020
New model type in MODFLOW 6
Developed in collaboration with Sorab Panday, GSI Environmental Inc.
Patterned after MT3D, USG-Transport, MODFLOW-GWT, SUTRA
Notes: What kind of modeler would I be if I didn’t put in an a partial differential equation…

## Slide 5: GWT Model Status
Available now in MODFLOW 6
Fully supported in FloPy
Theory report published
Represents a single species, BUT, can have any number of GWT Models
Transport across grids (new in 6.3.0)

## Slide 6
Mobile Storage and Transfer (MST)
Advection (ADV)
Dispersion (DSP)
Source and Sink Mixing (SSM)
Observations (OBS)
Constant Concentration (CNC)
Output Control (OC)
Discretization (DIS, DISV, DISU)
Initial Conditions (IC)
Immobile Storage and Transfer (IST)
Flow Model Interface (FMI)
Mass Source Loading (SRC)
Mobile Domain
Immobile Storage and Transfer (IST)
Immobile Storage and Transfer (IST)
Immobile Domain
Groundwater Transport (GWT) Model
Data Input
Transport/
Grid
Transport/
External
Transport/
Internal
Transport/
Internal
Transport/
Internal
Transport/
Internal
Streamflow Transport (SFT)
Multi-Aquifer Well Transport (MWT)
Lake Transport (LKT)
Transport/
Advanced Package
Unsaturated Zone Transport (UZT)
Mover Transport
(MVT)

## Slide 7: MODFLOW 6 GWF and GWT Approach (Option 1: Separate Simulations)
MODFLOW 6 GWF
MODFLOW 6 GWT
Concentration File(s)
Head File
Budget File
Simulation 1
Simulation 2
Can use different time-step lengths for GWT Model

## Slide 8: MODFLOW 6 GWF and GWT Approach (Option 2: Coupled Simulation)
MODFLOW 6 GWF/GWT
Concentration File(s)
Head File
Budget File
Simulation
Must use same time-step lengths for both models

## Slide 9: Variable-density simulations

## Slide 10: Coupled Variable-Density Flow and Transport
SEAWAT capabilities now available in MODFLOW 6
  Coupled variable-density flow and transport
Density can be a function of one or more solute concentrations
Bonus!
  Flexible unstructured meshes
  Newton-Raphson formulation
Notes: Provides SEAWAT capabilities plus much more (Newton, unstructured grid, advanced packages, …)

## Slide 11: Coupled Variable-Density Flow and Transport
Run GWF and GWT in same simulation
Turn on Buoyancy Package in GWF Model
Represent salt as a chemical species
Notes: Provides SEAWAT capabilities plus much more (Newton, unstructured grid, advanced packages, …)

## Slide 12: examples

## Slide 13: Advanced Packages and Water Mover
Notes: Concentrations after 25 years

## Slide 14: Surface and Groundwater Flow and Transport
Comparison between MODFLOW 6 (solid lines) and GWT (dashed lines)
Notes: Concentrations after 25 years

## Slide 15: Transport and Local Grid Refinement

## Slide 17: Coupled Flow and Transport Capabilities

## Slide 18: Coastal Aquifer Simulation
recharge
no flow
freshwater inflow
ocean boundary

## Slide 19: Spin-Up Boundary Conditions
recharge
recharge
recharge
recharge
general-head boundary

## Slide 20: Spin-Up Simulation

## Slide 21: Instantaneous SLR 1 m / 100 years

## Slide 22: Sea-Level Rise Boundary Conditions
recharge
R=R0*(1-fs)
recharge
recharge
recharge
general-head boundary (C=C0*fs)
general-head boundary
sx
sT
fs = sx/sT

## Slide 23: Sea-Level Rise Boundary Conditions
recharge
general-head boundary
general-head boundary
general-head boundary
sx
sT
fs = sx/sT
recharge
R=R0*(1-fs)
general-head boundary (C=C0*fs)

## Slide 24: Gradual SLR 1 m / 100 years

## Slide 25: Island Simulation

## Slide 26: Spin-Up Simulation

## Slide 27: Gradual SLR 1 m / 100 years