## Slide 1: McDonald Valley
A Model Calibration Exercise for MODFLOW

## Slide 2: Exercise Outline
Stage 1 – Planning phase
  Evaluate project objectives and develop conceptual model
Stage 2 – Initial model development
  Build MODFLOW dataset and calibrate model using existing data
Stage 3 – Improve model
  Collect new field data and refine model calibration
Stage 4 – Prediction phase
  Simulate development scenarios to evaluate project objectives

## Slide 3: Stage 3 – Improve Model
Data collection options
  Drill wells
    Shallow well (to a max of -100 ft)
    Deep well (to bedrock)
  Hydraulic tests
    Slug test (local value of horizontal K)
    Aquifer test (large scale value of K and possibly Kv)
      Can only be done on a new deep well
  Seismic Analysis
    N-S or E-W
    Bedrock elevation along that row/column
  Streamflow (baseflow) measurements
    Several points along Straight River

## Slide 4: Stage 3 – Improve Model
Budget: $200,000
Costs
  Drill wells
    Shallow well – $1,000
    Deep wells – $3,000
  Hydraulic tests
    Slug tests (limit of 7 on existing wells) – $250
    Aquifer test – $4,000 (including drilling)
  Seismic Section – $2,000
  Streamflow measurement – $500

## Slide 7: Stage 3 – Improve Model
Well in southern part of the valley at either of two sites
Well at Reilly’s Premium Beverages, Inc.
Objectives
  Limit drawdown to no more than 2 ft
  Limit stream flow reduction at Pollock’s Ford to less than 20%
  Do not induced infiltration along Straight River
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge