## Slide 1: Problem 1 Steady-state flow with constant head boundaries
Map View
Canal
River
W
E
10,000 feet
10,500 feet
0
200
220
330
320
W
E
Aquifer 1
Aquifer 2
silt
Cross Section View
Kh = 50 ft/d
Kv = 10 ft/d
Kh = Kv = 0.01 ft/d
Kh = 200 ft/d
Kv = 20 ft/d

## Slide 2: Problem 1 - MODFLOW Grid and Boundary Conditions
0
200
220
330
320
W
E
Layer 1 (Aquifer 1)
Layer 3 (Aquifer 2)
Layer 2 (silt)
Cross Section View
3 layers, 21 rows, 20 columns Horizontal grid cell size = 500 feet x 500 feet Canal simulated with constant head cells in in layer 1, column 1, rows 1 - 21 River simulated with constant head cells in layer 1, column 20, rows 1 – 21
No flow boundaries along the North, South, and Bottom
Map View

## Slide 3: Problem 1E and 1F Discontinuous Silt Layer
0
200
220
330
320
W
E
Aquifer 1
Aquifer 2
silt
Cross Section View
silt
Map View
Canal
River
W
E
10,000 feet
10,500 feet
no silt

## Slide 4: MODFLOW Data Files for Problem 1
mfsim.nam – MODFLOW Simulation name file
ps1.nam – Groundwater Flow Process name file
ps1.dis – Spatial Discretization package file
ps1.tdis – Time Discretization package file
ps1.ims – Iterative Model Solution package file
ps1.ic – Initial Conditions package file
ps1.chd – Constant Head package file
ps1.npf – Node Property Flow package file