## Slide 1: McDonald Valley
A Model Calibration Exercise for MODFLOW

## Slide 2: Exercise Outline
Stage 1 – Planning phase
  Evaluate project objectives and develop conceptual model
Stage 2 – Initial model development
  Build MODFLOW dataset and calibrate model using existing data
Stage 3 – Improve model
  Collect new field data and refine model calibration
Stage 4 – Prediction phase
  Simulate development scenarios to evaluate project objectives

## Slide 3: Study Area
Figure 1 – Regional Map
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 4: Proposed Groundwater Development
Well in southern part of the valley at either of two sites
Well at Reilly’s Premium Beverages, Inc.
County Cooperator
  Doesn’t want excessive water-table declines (no more than 2 ft)
  Must not reduce stream flow at Pollock’s Ford by more than 20%
  No induced infiltration at all along Straight River
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 5: Proposed Groundwater Development
County Cooperator – cont.
  Wants to regulate septic systems in northern part of valley
  Cooperator want the source area for groundwater into Lake Harbaugh
  Capture zone analysis of the Reilly well
  Capture zone analysis of the proposed Virginia City wells
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 6: McDonald Valley Study Area Information
Contains unconsolidated valley-fill alluvium (sands/gravels)
No hydraulic tests but estimated K ranges from 10-500 ft/day
Low permeability lake clay in some boreholes
Valley has 17 existing observations wells

## Slide 7: McDonald Valley Study Area Information
No significant seasonal or short-term fluctuations in conditions
Mean annual precipitation of 36 in/year
No surface-water inflow
Straight River
  Headwater stage = 1.8 ft
  Stage at end of valley = 0 ft
  Gradient is 0.0002 ft/ft
  100 ft wide and 1 ft deep
  Stream gages at end of valley and Pollock’s Ford
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 8: McDonald Valley Study Area Information
Lake Harbaugh
  Stage = 11 ft
  Area of the lake = 1.625 x 107 ft2
  Lake Evaporation = 27 in/year (2.25 ft/year)
  Precipitation = 36 in/year (3 ft/year)
  No surface-water inflow
  Steep sloping shore
  Uniform water depth of 16 ft
  Sandy bottom
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 9: Stage 1 – Planning Phase
Develop a conceptual model
  Contour water level data
  Elements of the system that are important?
  Decide how to model features
  Decide what boundary conditions to use
  Decide what vertical discretization to use
  Decide how to represent the Lake
    Constant Head Boundary
    General Head Boundary
    High hydraulic conductivity
  Decide how to represent recharge
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 10: Stage 1 – Planning Phase
Each team designs an approach for simulating McDonald Valley. After about 1 hour we will reconvene as a class and discuss the design plans.
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 12: Stage 1 – Planning Phase
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 13: Stage 1 – Planning Phase
Discussion
  How did you decide to represent the lake?
  How did you decide to represent recharge?
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 14: Stage 2 – Initial Model Development
Implement your conceptual model into a numerical model
Calibrate to existing conditions
  Adjust hydraulic parameters, boundary conditions so that model results are close to observations
    Adjust within justifiable ranges
    Avoid adjusting when it can’t be supported
Your model will be wrong, but hopefully will tell you something

## Slide 15: Stage 2 – Initial Model Development
Figure 1 – Regional Map
Figure 2 – Topographic Map of McDonald Valley
Lake
Harbaugh
L & H Lounge

## Slide 16: Stage 2 – Initial Model Development