## Slide 1: MODFLOW 6—XT3D
Introduction to Groundwater Modeling using MODFLOW
January 9-13, 2023
SDSU, San Diego California

## Slide 2: Challenge
Allow MODFLOW 6 to simulate groundwater flow with fully 3D anisotropy
Unstructured, cell-centered, finite-volume grids

## Slide 3: Representation of Anisotropy
Representation of full 3D anisotropy may be required for some problems (fractured aquifers, structurally deformed aquifers)
Some capabilities available but needed generalized CVFD method

## Slide 4: Hydraulic Conductivity Ellipsoid
Defined by three user-provided values on a cell by cell basis
For unrotated case,
  K11 = Kx
  K22 = Ky
  K33 = Kz
K11
K22
K33

## Slide 5: Ellipsoid Rotation
Users can optionally provide ANGLE1, ANGLE2, and ANGLE3 on a cell by cell basis
ANGLE1 is counter-clockwise rotation in the x, y plane

## Slide 6: Ellipsoid Rotation (cont.)
All three angles can be specified to represent ellipsoid orientation

## Slide 7: Effective Conductivity Approach
Large errors for certain ellipsoid configurations
Approximate, but relatively fast
Simple to implement

## Slide 8: Darcy’s Law with full 3D anisotropy

## Slide 9: Darcy’s Law with full 3D anisotropy
need all three components of head gradient
x component

## Slide 10: Gradient estimation - rectangular grid
x
y

## Slide 11: Gradient estimation - rectangular grid
x
y

## Slide 12: Gradient estimation - rectangular grid
x
y
spatial interpolation

## Slide 13: Gradient estimation - rectangular grid
x
y
x component

## Slide 14: Gradient estimation - rectangular grid
x
y
y component

## Slide 15: Gradient estimation - rectangular grid
x
y
average of two estimates

## Slide 16: Gradient estimation - rectangular grid
x
y
y component, other side

## Slide 17: Gradient estimation - rectangular grid
x
y
combine
estimates

## Slide 18: Gradient estimation - rectangular grid
x
y
weight by
distance

## Slide 19: Gradient estimation - rectangular grid
x
y
x
x
weight by
orientation

## Slide 20: Gradient estimation - rectangular grid
x
y

## Slide 21: Main ideas
Use weighted averaging to incorporate gradient information from neighboring connections

## Slide 22: Main ideas
Use weighted averaging to incorporate gradient information from neighboring connections
  Weight depends on distance

## Slide 23: Main ideas
Use weighted averaging to incorporate gradient information from neighboring connections
  Weight depends on distance
  Weight depends on orientation

## Slide 24: Main ideas
Use weighted averaging to incorporate gradient information from neighboring connections
  Weight depends on distance
  Weight depends on orientation
Combine estimates from both sides of the interface

## Slide 25: XT3D – regular and irregular grids

## Slide 26: XT3D – regular and irregular grids
spatial interpolation

## Slide 27: XT3D – regular and irregular grids
component along primary connection

## Slide 28: XT3D – regular and irregular grids
component along primary connection
“unknown” head

## Slide 29: XT3D – regular and irregular grids
component  to primary connection
= weighted average

## Slide 30: XT3D – regular and irregular grids
component  to primary connection
= weighted average
indirect information:
spatially removed from primary interface
components along neighboring connections (not )
need to do some math

## Slide 31: XT3D – regular and irregular grids
component  to primary connection
= weighted average
weight by:
distance: closer = more weight
indirect information:
spatially removed from primary interface
components along neighboring connections (not )
need to do some math

## Slide 32: XT3D – regular and irregular grids
component  to primary connection
= weighted average
weight by:
distance: closer = more weight
orientation: more  = more weight
x
indirect information:
spatially removed from primary interface
components along neighboring connections (not )
need to do some math

## Slide 33: XT3D – regular and irregular grids
component  to primary connection, other side

## Slide 34: XT3D – regular and irregular grids
combine estimates
(continuity of normal flux)

## Slide 35: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 36: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 37: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 38: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 39: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells
Larger stencil than in standard conductance-based MODFLOW formulation

## Slide 40: XT3D performance
Longer run times than standard MODFLOW formulation
Requires more memory than standard MODFLOW formulation
“RHS” suboption makes memory requirement comparable to default formulation (same stencil)

## Slide 41: Usage notes
To use XT3D, “flip a switch” in Node Property Flow (NPF) Package input
Matrix not necessarily symmetric  use BICGSTAB for linear acceleration
Don’t use ghost nodes (GNC) at the same time
Works with horizontal flow barriers (HFB)
Has a Newton-Raphson formulation
Vertical contribution to “conductances” currently based on fully saturated cell thickness

## Slide 42: Conclusions
XT3D handles arbitrarily oriented 3D anisotropy on structured and unstructured grids
“Ghost-node-like” correction on unstructured grids
Also applicable to dispersion